## Slide 1: Rezultatele activităţii de supraveghere desfăşurate în domeniul operaţiuni zbor Compartiment RAMP
1
1
ROMANIAN CIVIL AERONAUTICAL AUTHORITY
AACR - Ședință standardizare – București – Iunie 2018
Notes: In case of emergency, please use the door you came in because, even that we are at the ground floor, outside the windows is a quite deep ditch.
The emergency phone is of course, 112.

## Slide 2
2
RATA DE ȚARĂ (România)
Este rezultatul mediei ratelor operatorilor aerieni din România
RATA OPERATORULUI (de apariție a neconformităților)
Este rezultatul mediei ratelor de apariție a neconformităților constatate în urma inspecțiilor RAMP pentru aeronavele incluse în AOC
OBIECTIV
RATA DE ȚARĂ A ROMÂNIEI CÂT MAI MICA
RATE CÂT MAI MICI ALE OPERATORILOR AERIENI
AACR - Ședință standardizare – București – Iunie 2018

## Slide 3
3
AACR - Ședință standardizare – București – Iunie 2018
Mai 2016 | Sept 2016 | Ian 2017 | Mai 2017 | Sept 2017 | Ian 2018 | Mai 2018
0,59 | 0,71 | 0,77 | 0,95 | 0,82 | 0,81 | 0,56
Valorile Ratei de țară a României în ultimii 2 ani
Impactul ratei operatorului aerian asupra ratei de țară:
Creșterea ratei de țară de la 0,77 la 0,95 este rezultatul a două inspecții RAMP în cadrul cărora au fost constate mai multe neconformități de categorie 2 și 3

## Slide 4
4
AACR - Ședință standardizare – București – Iunie 2018
Acțiuni ca urmare a inspecțiilor RAMP
 | Type Of Action | Total | 2016 | 2017 | 2018
1 | Information to Captain | 399 | 146 | 164 | 89
2 | Information to the Authority and Operator | 111 | 39 | 44 | 28
3a | Restriction on the aircraft flight operation | 12 | 5 | 5 | 2
3b | Corrective actions before flight | 55 | 23 | 22 | 10
3c | Aircraft grounded by inspecting NAA | 0 | 0 | 0 | 0
3d | Immediate operating ban | 0 | 0 | 0 | 0
categoria 1 - Neconformităţi minore - raportate pilotului comandant
categoria 2 - Abateri semnificative de la standardele de siguranţă - raportate operatorului aerian şi autorităţii aeronautice de supraveghere a acestuia
categoria 3 - Impact major asupra siguranţei - este necesară corectarea neconformităţii înainte de decolare sau, după caz, impunerea unor restricţii de operare a aeronavei

## Slide 5
5
AACR - Ședință standardizare – București – Iunie 2018
Acțiuni ca urmare a inspecțiilor RAMP
    Pentru toate neconformităţile din categoriile 2 şi 3 autoritatea aeronautică care a efectuat inspecţia SAFA transmite o comunicare scrisă operatorului aerian, prin Baza de date centralizată SAFA a EASA în scopul solicitării de dovezi privind acţiunile corective
    Răspunsul operatorului aerian la comunicarea scrisă a autorităţii care a a efectuat inspecţia SAFA trebuie transmis în maxim 30 de zile
    Lipsa unei reacţii din partea operatorului poate fi interpretată ca „o lipsă a abilităţii şi/sau dorinţei unui operator aerian de a rezolva deficienţele legate de siguranţă”

## Slide 6
6
AACR - Ședință standardizare – București – Iunie 2018
Neconformități constatate în 2018
Cat | ITEM |  | FINDING DESCRIPTION
2 | A04 | Manuals | Incomplete parts of the Operations Manual pertaining to flight operations on board Emergency response guidance for incident involving dangerous goods- not on board
2 | A06 | Navigation / instrument charts | Required en-route charts out of date (navigation database up to date) EFB Terminal charts (captain) not updated on incoming flight F/O EFB up to date and pper version present. problem solved for outbound flight. -
2 | A07 | Minimum Equipment List | Some MEL items not fully customised (but no defects affecting those items) examples- 34-15, 34-16 , 34-40
3 | A10 | AOC or equivalent | Commercial Air Transport operations not in accordance with the operations specifications Shipment described under D02 loaded whilst the operator has not been granted DG special approval according to Ops Specs
2 | A13 | Flight Preparation | Content and use of the Operational Flight plan not in accordance with the operations manual No flight performance details mentioned on the OFP, e.g. time of departure (actual off-block time); time of arrival (on-block time); route segments with actual time; no in-flight fuel monitoring was recorded as required by the OM (flight time 1 hour, i.a.w. ATLB and OFP). Ref.: AMC1 CAT.OP.MPA.175(a)

## Slide 7
7
AACR - Ședință standardizare – București – Iunie 2018
Neconformități constatate în 2018
Cat | ITEM |  | FINDING DESCRIPTION
2 | A14 | Mass and balance calculation | Incorrect mass and/or balance calculations, within a/c limits, and having minor effect on the performance calculations.TO data computation (ActTOM/index) incorrect; - Total fuel on board 2350 kg, Taxi fuel 50kg, TOF has to be 2300kg instead of 2050kg; - Allowed Mass for TO incorrect; Max LM used 20350kg instead of 22350kg, as well as TOF used 2050kg instead of 2300kg; - Balance calculation not completed / correct; there are no balances for TOM and LM mentioned on the graphic to proof if the balance is in operational envelop.
2 | A14 | Mass and balance calculation | Incorrect mass and/or balance calculations, within a/c limits, and having minor effect on the performance calculations.Take off fuel 3200 kg did not take into account the taxi fuel of 45 kg. Within a/c limits, minor effect on aircraft performance.
3 | A17 | Harness | No or unserviceable safety harness for each active crew seat (outside dispatch limits/conditions) On co-pilot seat automatic restraining device (Inertia Reels) found unserviceable. After temporary repair and according to MEL 10-1-1 where repairs or replacement are carried out within three calendar days, aircraft release to departure. Defect is entered in ATL Log No. 0790
2 | A20 | Flight crew licence / composition | Pilot(s) having obvious difficulty speaking in English, despite holding a valid ELP endorsement Co-pilot having obvious difficulty speaking english, despite holding a valid ELP endorsement (Level 4) -

## Slide 8
8
AACR - Ședință standardizare – București – Iunie 2018
Neconformități constatate în 2018
Cat | ITEM |  | FINDING DESCRIPTION
2 | A23 | Defect notification and rectification (incl. Tech log) | Known defect not reported/assessed See item : C01 (remark on speed tape covering screws)
2 | A23 | Defect notification and rectification (incl. Tech log) | No evidence of identification nor monitoring of significant defect See item : C02
2 | A23 | Defect notification and rectification (incl. Tech log) | No evidence of identification nor monitoring of significant defect See C01 (structural item). Significant doubts that external damage chart item No. 11 (discribed as aft of cargo door 1) is matching the structural dent found just in front of cargo door No. 2. Therefore homebase verifcation required on the basis of frame and stringer count
3 | A23 | Defect notification and rectification (incl. Tech log) | Required maintenance action not performed or not in accordance with applicable (MEL/AMM/SRM) instructions See item C07
2 | A23 | Defect notification and rectification (incl. Tech log) | Known defect not reported/assessed See C01 for details

## Slide 9
9
AACR - Ședință standardizare – București – Iunie 2018
Neconformități constatate în 2018
Cat | ITEM |  | FINDING DESCRIPTION
2 | A23 | Defect notification and rectification (incl. Tech log) | Maintenance action not properly reported Abradable shroud Eng. #2 missing material at pos." 6 o`clock". Reported, repaired and released numerous times according to operators "Structural damage & Repair list" found in A/C techlog. Evidently last repair also without succsess. Last release action entry is not readable for SACA inspector nor Captain. Operators Technical Department contacted and they confirmed that abredable shroud shall be repaired within 50 cycles after last release in tech log. This confirmed by operator to be in accordance with TC holder`s documentation.
2 | A23 | Defect notification and rectification (incl. Tech log) | Maintenance action not properly reported See D01 -
3 | A23 | Defect notification and rectification (incl. Tech log) | Technical logbook entry not understood by the flight crew members TCAS antenna u/s defect was written but in fact tcas system was functioning on/off, deferal of the defect was done inappropriately

## Slide 10
10
AACR - Ședință standardizare – București – Iunie 2018
Neconformități constatate în 2018
Cat | ITEM |  | FINDING DESCRIPTION
3 | B01 | General Internal Condition | Covers damaged/missing exposing sharp edges and/or cables and wires Plastic knee protection missing at row 10 E/F and broken at row 16 E/F (see attached photos)
2 | B01 | General Internal Condition | Equipment installations obviously not in compliance with Annex 8, Part IIIA/B, Chapter 4 fwd and aft galleys food carts size are not suitable for the specific aircraft. they can not be locked properly with galleys red locks. water bottles were stored behind food carts- photo attached.
3 | B01 | General Internal Condition | Galley/lavatory waste receptacle access door cover inoperative (outside dispatch limits/conditions) aft galley right waste compartment door cover - does not close-photo attached.
3 | B06 | Seat belt and seat condition | Seat(s) unserviceable and not identified as such Seat belts of seat 6D, 19C and 22B damaged (edge cut and hole).
3 | B06 | Seat belt and seat condition | Seat(s) unserviceable and not identified as such Cushion of seat 12F (overwing emergency exit row) not sticking to seat frame due to worn-out velcro straps. -

## Slide 11
11
AACR - Ședință standardizare – București – Iunie 2018
Neconformități constatate în 2018
2 | B07 | Emergency exit, lighting, Independent portable light | Some of the cabin crew members have no serviceable portable light available/ readily accessible One of the cabin crew members at cabin crew seat door 2R with unserviceable flashlight (fitted but not charging) -
2 | B09 | Oxygen Supply (Cabin Crew and Passengers) | Oxygen equipment not immediately available and required for the type of flight Oxygen masks are not pre-attached to oxygen bottles located in cabin. Reference from CS 25 (book 1): (4) Portable oxygen equipment must be immediately available for each cabin crew member. The portable oxygen equipment must have the oxygen dispensing unit connected to the portable oxygen supply.(See AMC 25.1447(c)(4)) book 2 states: CS-25 BOOK 2 -F-218 AMC 25.1447(c)(4) Equipment Standards for Oxygen-Dispensing Units 1 The equipment should be so located as to be within reach of the cabin crewmembers while seated and restrained at their seat stations. 2 The mask/hose assembly should be already connected to the supply source, and oxygen should be delivered with no action being required except turning it on and donning the mask. 3 Where a cabin crewmember's work area is not within easy reach of the equipment provided at his seat station, an additional unit should be provided at the work area.
2 | B12 | Access to emergency exits | Damaged wall panel in the vicinity of emergency exit possibly obstructing the exit Lights control access cover quick release latches are torn. Tape applied for fixing but partly missing at the time of inspection.Therefore cover is loose means possible obstruction for legs during an evacuation.
Cat | ITEM |  | FINDING DESCRIPTION

## Slide 12
12
AACR - Ședință standardizare – București – Iunie 2018
Neconformități constatate în 2018
Cat | ITEM |  | FINDING DESCRIPTION
3 | C01 | General External Condition | Fasteners or rivets loose or missing outside dispatch limits/conditions Four fasteners in a row missing at the belly fairing panel near drain mast aft of the wheel well on the left hand side. In addition one fastener missing at the panel on the left hand belly fairing below leading edge of the wing
2 | C02 | Doors and Hatches | Door handle(s), lever(s), access panel(s) not flush Upon aircraft arrival, aft cargo door handle found not fully stowed. Door correctly locked. -
2 | C02 | Doors and Hatches | Door handle(s), lever(s), access panel(s) not flush Misaligned door on access to cargo door control panel. -
2 | C05 | Undercarriage, skids/floats | Safety markings not applied or unreadable LH MLG tyre service placard worn (upgraded after review) -
3 | C07 | Powerplant and Pylon | Panels/fairings/cowlings/handles misaligned or not flush outside dispatch limits/conditions Engine #2 FWD pylon one latch not correctly closed, red indicator marking visible -
3 | C07 | Powerplant and Pylon | Panels/fairings/cowlings/handles misaligned or not flush outside dispatch limits/conditions One of 2 latches of the aft cowlings (bottom side) engine No 1 at open position on arrival. See photo. -

## Slide 13
13
AACR - Ședință standardizare – București – Iunie 2018
Neconformități constatate în 2018
Cat | ITEM |  | FINDING DESCRIPTION
3 | D03 | Cargo stowage | Load distribution/load limit (floor and/or height) exceeded During the inspection on a/c arrival, the rear cargo compartment was found to be loaded by exceeding the height limit.
3 | D03 | Cargo stowage | Cargo not correctly secured and restrained in all directions fwd cargo compartement Fly away kit-
2 | E01 | General | Aircraft not operated in accordance with manufacturer standards - metal weight relief hook of electrical power cable attached to aircraft structure
3 | E01 | General | No cabin attendant able to speak and understand Italian language.

## Slide 14
14
AACR - Ședință standardizare – București – Iunie 2018
Acțiuni preventive - exemple
Elaborarea, în cadrul operatorului aerian, a unei proceduri pentru preîntâmpinarea neconformităților la inspecțiile RAMP
Instruirea echipajelor asupra aspectelor pe care se pune accent la o inspecție RAMP, astfel încât să fie pregătite să răspundă întrebărilor inspectorilor, inclusiv în ceea ce privește toată documentația aflată la bord
Controlul riguros al tuturor înregistrărilor legate de întreținerea aeronavei
Instruirea echipajelor de cabină privind verificarea cabinei de pasageri, a echipamentelor de urgență și a altor elemente de siguranță înainte de fiecare zbor (inclusiv la escală), precum și raportarea și înregistrarea imediată a tuturor defectelor constatate
Verificarea modului de încărcare a calelor de bagaje și de închidere a ușilor/panourilor exterioare ale aeronavei înainte de fiecare zbor

## Slide 15: ATENTIE – Informare pentru echipaje
Unele dintre statele UE au adoptat în legislația națională dreptul de control privind consumul de alcool și/sau droguri pentru echipaje, altele decat cele ale operatorilor aerieni naționali
Dintre acestea, Germania a trecut la efectuarea acestor controale în cadrul inspecțiilor RAMP
Asemenea controale sunt de așteptat și la escale în Italia, Olanda, Suedia, Franța
Atenție la abordarea acestui gen de controale de către echipaje - Refuzul de a se supune controlului poate duce la întârzierea sau chiar anularea zborului
AACR - Ședință standardizare – București – Iunie 2018

## Slide 16
16
AACR - Ședință standardizare – București – Iunie 2018