## Slide 1: – TRANSPORTUL DE BUNURI PERICULOASE – Prevederi comune indiferent daca operatorul aerian DEȚINE sau NU DEȚINE autorizație de transport
1
1
Vicențiu DINU
Inspector aeronautic
CN-TABP
DOACP-SOA-CBP
ROMANIAN CIVIL AERONAUTICAL AUTHORITY
AACR - Ședință standardizare – București – Iunie 2018

## Slide 2
2
2
ROMANIAN CIVIL AERONAUTICAL AUTHORITY
27 iunie 2018
Chapter 9:
9.1 Dangerous Goods
General
Policy on the Transport of Dangerous Goods
Limitation
Provision of Information
Classification, Marking and Labeling
Duties of All Personnel Involved
Documents
Recognition of Undeclared / Hidden Dangerous Goods
Operation Manual: OM-A

## Slide 3
3
3
ROMANIAN CIVIL AERONAUTICAL AUTHORITY
27 iunie 2018
Chapter 9:
9.2 CONDITIONS UNDER WHICH WEAPONS, MUNITIONS OF WAR AND SPORTING WEAPONS MAY BE CARRIED
Transport of weapons of war and munitions of war
Carriage of sporting weapons and sporting ammunition
Chapter 11:
11.10 Special Notification Requirements in the Event of an Accident or Occurrence
Operation Manual: OM-A

## Slide 4
4
4
ROMANIAN CIVIL AERONAUTICAL AUTHORITY
27 iunie 2018
Chapter 2.4 Training syllabus for transport of dangerous goods
Approval of training programme
General requirements applicable to dangerous goods training programme
Dangerous goods training syllabus
Instructor qualifications
Identification of training and testing materials
Operation Manual: OM-D

## Slide 5
5
5
ROMANIAN CIVIL AERONAUTICAL AUTHORITY
27 iunie 2018
1. General
Decision of operator to use the ICAO or IATA regulation
The text from this paragraph must make numerous references to the International Civil Aviation Organization’s Technical Instructions for the Safe Transport of Dangerous Goods by Air (Technical Instructions). Should the Operator have decided to use the IATA Dangerous Goods Regulations in lieu of the ICAO Technical Instructions, references to the ICAO Technical Instructions should be amended accordingly.
Operation Manual: OM-A Ch. 9.1

## Slide 6
6
6
ROMANIAN CIVIL AERONAUTICAL AUTHORITY
27 iunie 2018
2. Policy on the Transport of Dangerous Goods
Approval for the Transport of Dangerous Goods (CAT.GEN.MPA.200, SPA.DG.105)
  General information;
  Declaration of operator if it holds, or not, an approval for the transport of dangerous goods by air;
Operation Manual: OM-A Ch. 9.1

## Slide 7
7
7
ROMANIAN CIVIL AERONAUTICAL AUTHORITY
27 iunie 2018
3. Limitation
a) General Exceptions
  Airworthiness and Operational Items (CAT.GEN.MPA.200 (b)(1));
  Veterinary Aid (CAT.GEN.MPA.200 (b)(1));
  Medical Aid for a Patient (CAT.GEN.MPA.200 (b)(1));
  Excess baggage being sent as cargo;
  Items That May Be Carried by Passengers and Crew (CAT.GEN.MPA.200 (b)(2)).
Operation Manual: OM-A Ch. 9.1

## Slide 8
8
8
ROMANIAN CIVIL AERONAUTICAL AUTHORITY
27 iunie 2018
3. a) i) Airworthiness and Operational Items
  An approval is not required for dangerous goods which are required to be aboard the aircraft such as:
  a) items for airworthiness or operating reasons or for the health of passengers or crew;
  b) aerosols, alcoholic beverages, perfumes, colognes, liquefied gas lighters and portable electronic devices containing lithium metal or lithium ion cells or batteries carried aboard an aircraft by the operator for use or sale on the aircraft during the flight or series of flights, but excluding non-refillable gas lighters and those lighters liable to leak when exposed to reduced pressure; and
  c) dry ice intended for use in food and beverage service aboard the aircraft; and
  d) electronic devices such as electronic flight bags, personal entertainment devices, credit card readers, containing lithium metal or lithium ion cells or batteries and spare lithium batteries for such devices carried aboard an aircraft by the operator for use on the aircraft during the flight or series of flights, provided that the batteries meet the provisions applicable to the carriage of portable electronic devices containing lithium or lithium ion cells or batteries by passengers. Spare lithium batteries must be individually protected so as to prevent short circuits when not in use.
  .
Operation Manual: OM-A Ch. 9.1
Notes: cum ar fi bateriile, stingătoarele de incendiu, trusele de prim ajutor, insecticidele, odorizatoarele de aer, plutele de salvare, diapozitivele de salvare, dispozitivele de salvare, consumabilele portabile de oxigen, semnele de tritiu, hotele de fum
cu condiția ca bateriile să respecte dispozițiile aplicabile atunci când sunt transportate de pasageri și echipaj
d) Condițiile pentru transportul și utilizarea acestor dispozitive electronice și pentru transportul bateriilor de rezervă trebuie furnizate în manualul operațional și / sau în alte manuale adecvate, ceea ce le va permite echipajului de zbor, echipajului de cabină și altor angajați să-și îndeplinească responsabilitățile. Operatorii ar trebui fie să explice aceste condiții, fie să specifice că nu pot fi transportate piese de schimb.
ATENȚIE!!! Orice produs care se transportă în vederea înlocuirii se supune prevederilot unei Aprobari de transport bunuri periculoase!

## Slide 9
9
9
ROMANIAN CIVIL AERONAUTICAL AUTHORITY
27 iunie 2018
3. a) ii) Veterinary Aid
  An approval is not required for dangerous goods which are carried for use in flight as veterinary aid or as a humane killer for an animal. Such dangerous goods must be stowed and secured during take-off and landing and at all other times when deemed necessary by the pilot-in-command. The dangerous goods must be under the control of trained personnel during the time when they are in use on the aircraft.
  Dangerous goods may be carried on a flight made by the same aircraft before or after a flight for which they are required as veterinary aid or as a humane killer for an animal, (e.g. training flights and positioning flights prior to or after maintenance), when it is impracticable to load or unload the dangerous goods immediately before or after the flight
Operation Manual: OM-A Ch. 9.1
Notes: CONDIȚII:
a) mărfurile periculoase trebuie să poată rezista condițiilor normale de transport aerian;
b) mărfurile periculoase trebuie să fie identificate corespunzător (de exemplu, prin marcare sau etichetare);
c) mărfurile periculoase pot fi transportate numai cu aprobarea operatorului;
d) mărfurile periculoase trebuie inspectate pentru daune sau scurgeri înainte de încărcare;
e) încărcarea trebuie supravegheată de operator;
f) mărfurile periculoase trebuie să fie arimate și fixate în aeronavă într-un mod care să împiedice orice mișcare în zbor care să le modifice orientarea;
g) comandantul-comandant trebuie să fie informat despre mărfurile periculoase încărcate la bordul aeronavei și locația lor de încărcare. În cazul schimbării echipajului, aceste informații trebuie transmise echipajului următor;
h) întregul personal trebuie să fie instruit proporțional cu responsabilitățile lor; și
i) se aplică dispozițiile privind Raportarea accidentelor și incidentelor cu bunuri periculoase.

## Slide 10
10
10
ROMANIAN CIVIL AERONAUTICAL AUTHORITY
27 iunie 2018
3. a) iii) Medical Aid for a Patient
  An approval is not required for dangerous goods which:
  a) are placed on board an aircraft with the approval of the operator; or
  b) form part of the permanent equipment of the aircraft when it has been adapted for specialized use, to provide, during flight, medical aid for a patient, such as gas cylinders, drugs, medicines, other medical material (e.g. sterilising wipes) and wet cell or lithium batteries.
  These dangerous goods may also be carried on a flight made by the same aircraft to collect a patient or after that patient has been delivered (e.g. training flights and positioning flights prior to or after maintenance), when it is impracticable to load or unload the goods at the time of the flight on which the patient is carried.
Operation Manual: OM-A Ch. 9.1
Notes: Condiții pentru b)
i) buteliile de gaz au fost fabricate special pentru a conține și a transporta gazul respectiv;
ii) medicamentele și medicamentele și alte materii medicale sunt sub controlul personalului instruit în timpul utilizării;
(iii) echipamentul care conține baterii cu celule umede este păstrat și, atunci când este necesar, fixat, într-o poziție verticală pentru a împiedica scurgerea electrolitului; și
iv) se prevede o asigurare adecvată pentru a depozita și a asigura tot echipamentul în timpul decolării și aterizării și în orice alt moment când comandantul consideră necesar acest lucru în interesul siguranței.
Bunurile periculoase transportate pot diferi de cele identificate mai sus datorită nevoilor pacientului. Aceste dispoziții se aplică atât ambulanțelor de aer dedicate, cât și aeronavelor modificate temporar.

## Slide 11
11
11
ROMANIAN CIVIL AERONAUTICAL AUTHORITY
27 iunie 2018
3. a) iv) Excess baggage being sent as cargo
  An approval is not required for dangerous goods contained within items of excess baggage being sent as cargo provided that:
    i) the excess baggage has been consigned as cargo by or on behalf of a passenger;
    ii) the dangerous goods may only be those that are permitted by and in accordance with 9.1.5 to be carried in checked baggage; and
    iii) the excess baggage is marked with the words “Excess baggage consigned as cargo”.
  With the aim of preventing dangerous goods, which a passenger is not permitted to have, from being taken aboard an aircraft in excess baggage consigned as cargo, any organization or enterprise accepting excess baggage consigned as cargo should seek confirmation from the passenger, or a person acting on behalf of the passenger, that the excess baggage does not contain dangerous goods that are not permitted and seek further confirmation about the contents of any item where there are suspicions that it may contain dangerous goods that are not permitted.
Operation Manual: OM-A Ch. 9.1
Notes: Nu este necesară o aprobare pentru ca mărfurile periculoase conținute în articolele de bagaje în exces să fie trimise ca mărfuri cu condiția ca:
i) bagajele în exces au fost expediate ca mărfuri de către sau în numele unui pasager;
ii) mărfurile periculoase nu pot fi decât cele care sunt permise de către și în conformitate cu punctul 9.1.5 să fie transportate în bagajele înregistrate; și
iii) bagajele în exces sunt marcate cu mențiunea "Bagaj excesiv expediat ca marfă".
În scopul prevenirii ca mărfurile periculoase, pe care nu le este permis un pasager, să fie luate la bordul unei aeronave în exces de bagaje expediate ca mărfuri, orice organizație sau întreprindere care acceptă bagajele în exces expediate ca marfă ar trebui să solicite confirmarea de la pasager sau o persoană acționând în numele pasagerului că bagajele în exces nu conțin mărfuri periculoase care nu sunt permise și căutând o confirmare suplimentară cu privire la conținutul oricărui articol în cazul în care există suspiciuni că acesta ar putea conține mărfuri periculoase care nu sunt permise.

## Slide 12
12
12
ROMANIAN CIVIL AERONAUTICAL AUTHORITY
27 iunie 2018
3. a) v) Items That May Be Carried by Passengers and Crew
This item applies to all air operators, whether they hold or not approval for transport of dangerous goods.
Aspects related to this subject may be included in Chapter 9 or treated as independent procedures or points in other associated manuals. Regardless of how they are presented, procedures must be sent to authority and approved.
However, for dangerous goods for which approval by the operator is required, the operator must make specific procedures for:
  informing the passenger,
  receiving the application and related documents / information,
  analyzing the application for the approval of the goods,
  the company's decision to approve or refuse,
  the way to provide the operator decision to passenger, and
  checking the compliance of the products at the arrival of the passenger at check-in;
  Final decision
Operation Manual: OM-A Ch. 9.1

## Slide 13
13
ROMANIAN CIVIL AERONAUTICAL AUTHORITY
27 iunie 2018
Depending on the instructions used (ICAO or IATA), the table and related information on this topic will take different forms of presentation:
  ICAO
Operation Manual: OM-A Ch. 9.1
The information in this table is sufficient to describe dangerous goods and transport conditions.

## Slide 14
14
14
ROMANIAN CIVIL AERONAUTICAL AUTHORITY
27 iunie 2018
  IATA
Operation Manual: OM-A Ch. 9.1
The information in this table is NOT sufficient to describe dangerous goods and transport conditions.
This table should be completed with other information described in chapter 2.3 of the IATA-DGR.

## Slide 15
15
15
ROMANIAN CIVIL AERONAUTICAL AUTHORITY
27 iunie 2018
3. Limitation (continuing)
b) Dangerous goods in property of operator
  The procedure by which the operator's personnel must recognize the dangerous goods included in the COMAT category so that the company's policy (to transport / not carry dangerous goods) can be respected must be stated and specified.
  It should be specified that the personnel involved in the COMAT processing must have adequate training in accordance with the company policy.
Operation Manual: OM-A Ch. 9.1

## Slide 16
16
16
ROMANIAN CIVIL AERONAUTICAL AUTHORITY
27 iunie 2018
4. Provision of Information
Information to Passengers (CAT.GEN.MPA.200 (f))
  Ticketing
  Check-in
  Gate
Information at Cargo Acceptance Areas (CAT.GEN.MPA.200 (g))
Operation Manual: OM-A Ch. 9.1

## Slide 17
17
17
ROMANIAN CIVIL AERONAUTICAL AUTHORITY
27 iunie 2018
5. Classification, Marking and Labeling
  General presentation of classification, codification (especial for IATA), marking and labeling
Operation Manual: OM-A Ch. 9.1

## Slide 18
18
18
ROMANIAN CIVIL AERONAUTICAL AUTHORITY
27 iunie 2018
6. Duties of All Personnel Involved (CAT.GEN.MPA.200 (d))
Detailed Assignments of Responsibilities:
Cargo Department/ Cargo Sales Agents
Persons receiving or handling general cargo, mail and stores
Persons receiving or handling dangerous goods
Reservations
Persons handling passengers
Cabin Crew
Operations Personnel
Flight Crew
Trainers
Compliance Monitoring Manager, Auditors and Safety Manager
Operation Manual: OM-A Ch. 9.1

## Slide 19
19
19
ROMANIAN CIVIL AERONAUTICAL AUTHORITY
27 iunie 2018
7. Documents
Notification to Captain (NOTOC) (SPA.DG.110, AMC SPA.DG.110(a) )
  NOTOC complement in terms of dangerous goods carried by passengers that requires informing the pilot in command.
  The procedure will be detailed:
  Item must contain;
  Forms available used by operator;
  Availability of NOTOC on the Ground for the Duration of Flight
Retention of Documents (ORO.MLR.115 (b)(4), SPA.DG.110(f))
Operation Manual: OM-A Ch. 9.1

## Slide 20
20
20
ROMANIAN CIVIL AERONAUTICAL AUTHORITY
27 iunie 2018
8. Recognition of Undeclared / Hidden Dangerous Goods (CAT.GEN.MPA.200 (e))
List of general description of shipments which can contain hidden dangerous goods
Different kind of recognition of undeclared / hidden dangerous goods
Identification of Dangerous Goods Through X-Ray Screening
Safety Data Sheets
Consumer Labelling
  GHS Labels (ICAO Doc. 9284 ref. 7;1.1.2 Note 1, or IATA DGR 2;2.2.2 Note & Appendix B.4)
  CHIP Labels
Operation Manual: OM-A Ch. 9.1
Notes: Unele obiecte de uz casnic de zi cu zi poartă etichete de avertizare pentru consumatori, care pot indica sau nu că sunt clasificate ca mărfuri periculoase în transportul aerian. În întreaga lume există diferite legi privind modul de identificare a proprietăților periculoase ale substanțelor chimice (denumită "clasificare") și modul în care informațiile despre aceste pericole sunt apoi transmise utilizatorilor (prin etichetele de furnizare a consumatorilor și fișele tehnice de securitate pentru lucrători). Acest lucru poate fi confuz, deoarece aceeași substanță chimică poate avea descrieri diferite de pericole în diferite țări. De exemplu, un produs chimic ar putea fi etichetat pentru a fi furnizat ca "toxic" într-o țară, dar nu în altul. Din acest motiv, ONU a reunit experți din diferite țări pentru a crea Sistemul global armonizat de clasificare și etichetare a produselor chimice (GHS).
În Europa, Regulamentul privind clasificarea, etichetarea și ambalarea substanțelor și amestecurilor (cunoscut sub numele de Regulamentul CLP) prevede o perioadă de tranziție care să permită o migrare treptată la regimul GHS. Regulamentul se aplică deja clasificării substanțelor și se aplică amestecurilor începând cu 1 iunie 2015. Între timp, furnizorii pot continua să eticheteze (CHIP) mărfurile în conformitate cu regulamentele privind produsele chimice (Informații privind pericolele și ambalarea pentru furnizare). Cu toate acestea, aceștia pot alege ca alternativă clasificarea, etichetarea și ambalarea amestecurilor în conformitate cu CLP. Există, prin urmare, două sisteme de etichetare a aprovizionării cu consumatori care pot indica prezența mărfurilor periculoase.

## Slide 21
21
21
ROMANIAN CIVIL AERONAUTICAL AUTHORITY
27 iunie 2018
8. Recognition of Undeclared / Hidden Dangerous Goods (CAT.GEN.MPA.200 (e))
e) Consumer Labelling
Operation Manual: OM-A Ch. 9.1
GHS | CHIP |  | GHS | CHIP |  | GHS | CHIP |  | GHS | CHIP
Notes: Etichetele CHIP pentru amestecuri vor fi înlocuite cu sistemul de armonizare globală (GHS) a etichetării la 1 iunie 2015.
Informațiile privind CHIP ar trebui eliminate după 1 iunie 2017 odată ce măsurile de tranziție nu mai sunt aplicabile.
Tabelul de mai sus nu se aplică substanțelor și preparatelor din diviziunea 6.2 și clasa 7 care nu fac obiectul Regulamentului CHIP.

## Slide 22
22
22
ROMANIAN CIVIL AERONAUTICAL AUTHORITY
27 iunie 2018
1. Transport of weapons of war and munitions of war
Need for Approval to Transport Weapons and ammunitions of War (CAT.GEN.MPA.155)
Stowage Requirements for Weapons and ammunitions of War (EC Regulation 300/2008)
Notification of Commander of the Carriage of Weapons and ammunitions of War (CAT.GEN.MPA.155)
Carriage of Sporting Weapons and Ammunition When Inaccessible to Passengers During Flight (CAT.GEN.MPA.160)
Operation Manual: OM-A Ch. 9.2

## Slide 23
23
23
ROMANIAN CIVIL AERONAUTICAL AUTHORITY
27 iunie 2018
Special notification requirements in the event of an accident or occurrence when dangerous goods are being carried or have been offered for air transport without having been prepared and declared in accordance with the ICAO Technical Instructions. (it is necessary links with the paragraph from chapter 9)
Information to be provided by the operator in the event of an aircraft accident or serious incident where dangerous goods carried as cargo may be involved
Information to be Provided by the Operator in the Event of an Aircraft Incident (CAT.GEN.MPA.200(e))
Operation Manual: OM-A Ch. 11.10

## Slide 24
24
24
ROMANIAN CIVIL AERONAUTICAL AUTHORITY
27 iunie 2018
Dangerous Goods Accident and Incident Reports (CAT.GEN.MPA.200(e))
  Definitions of:
    Dangerous goods accident
    Dangerous goods incident
  Connection with ICAO Annex 13, ORO.GEN.160, Regulation (EU) No. 376/2014
  Report Form
Removal of Contamination (SPA.DG.105)
Operation Manual: OM-A Ch. 11.10

## Slide 25
25
25
ROMANIAN CIVIL AERONAUTICAL AUTHORITY
27 iunie 2018
1. Approval of training programme (ORO.GEN.110(j))
Statement on the authorization of training programs in the carriage of dangerous goods by air in accordance with ORO.GEN.110(j).
Statement of preparation at the company's internal training center, authorized under PIAC-TABP, or in external training centers (prior to outsourcing the provision of dangerous goods training, operators must establish that the proposed training materials are approved by the Authority).
Operation Manual: OM-D Ch. 2.4

## Slide 26
26
26
ROMANIAN CIVIL AERONAUTICAL AUTHORITY
27 iunie 2018
2. General requirements applicable to dangerous goods training programme
Statement on the need initial and recurrent training of all staff involved in direct or indirect activities of transport of dangerous goods;
Specifying the validity of courses and where new training can take place;
The records of training must be retained by the employer for a minimum period of 36 months;
Records must be made available upon request to the employee or the appropriate national authority.
Operation Manual: OM-D Ch. 2.4

## Slide 27
27
27
ROMANIAN CIVIL AERONAUTICAL AUTHORITY
27 iunie 2018
3. Dangerous goods training syllabus
The areas to be covered for various categories of personnel must be listed in a table; the depth of training required for each area is dependent on the responsibilities of the individuals and varies from a general appreciation to in-depth knowledge so that decisions can be taken.
Syllabus should be presented for all categories of staff with responsibility as outlined in Chapter 9 of OM-A
If a staff category is not clearly defined in accordance with ICAO Doc 9284 and IATA-DGR will choose a predefined Cat personnel category so that it covers the duties of staff concerned.
Operation Manual: OM-D Ch. 2.4

## Slide 28
28
28
ROMANIAN CIVIL AERONAUTICAL AUTHORITY
27 iunie 2018
4. Instructor qualifications
Instructors of initial and recurrent dangerous goods training programme must have adequate instructional skills and have successfully completed a dangerous goods training programme in the applicable category, or Category 6, prior to delivering such a dangerous goods training programme.
Instructors delivering initial and recurrent dangerous goods training programme must at least every 24 months deliver such courses, or in the absence of this attend recurrent training.
The above information does not apply to the exclusive use of Computer-Based Training (CBT) and other self-study materials for the delivery of dangerous goods training, i.e. where none of the training is delivered in person. There must, however, exist adequate means to ensure that persons creating and maintaining self-study training materials are competent and their knowledge of the transport of dangerous goods by air remains current.
Operation Manual: OM-D Ch. 2.4

## Slide 29
29
29
ROMANIAN CIVIL AERONAUTICAL AUTHORITY
27 iunie 2018
5. Identification of training and testing materials
All kind of information and materials concerning training, initial or recurrent, for each personnel category
Examples of tests for all kind of courses.
Operation Manual: OM-D Ch. 2.4

## Slide 30
30
Thanks!
27 iunie 2018